## Slide 1
IREC 2026 | Podium Session
Aeroelastic Stability Analysis of
Composite Fins on a 30,000 ft
COTS Sounding Rocket
Using High-Fidelity Computational Methods: CLT · Shell FEM · Supersonic Piston Theory
Team
207
Institution
ITBA
Category
30k ft COTS
Buenos Aires, Argentina • 2026

## Slide 2
Presentation Roadmap
2 / 13
Team 207 • ITBA • IREC 2026
01
Problem Statement
Why fin flutter is the critical aeroelastic failure mode for supersonic rockets
02
Physical System
Flight-hardware fin geometry, T700/epoxy laminate, and flight envelope
03
Theoretical Framework
Classical Lamination Theory · Shell FEM · Supersonic Piston Theory
04
Solver Architecture
Eight-step MATLAB pipeline with ISA atmosphere and eigenvalue flutter solver
05
Key Results
Natural frequencies, flutter envelope, and SM=∞ across 246 supersonic points
06
Physical Interpretation
Dual wash-out: geometric sweep + material D₁₆ bending-torsion coupling
07
Conclusions
Design validation and IREC 2026 flight test expectations

## Slide 3
Problem Statement: Why Flutter Matters
Aeroelastic instability is the critical structural risk in supersonic rocketry
3 / 13
Team 207 • ITBA • IREC 2026
Fin flutter is a catastrophic aeroelastic instability in which aerodynamic forces couple with structural vibration modes to produce divergent, self-sustaining oscillations.
Above the critical flutter speed, oscillation amplitudes grow exponentially — fin structural failure occurs within milliseconds.
For a 30,000 ft COTS rocket, the fin must remain stable throughout the full supersonic phase (Mach 1.0 – 1.85) without any passive protection mechanism.
!
Structural Failure
Fin detachment destroys vehicle aerodynamic stability
↑
Speed Dependency
Risk increases nonlinearly above flutter onset Mach number
✓
Design Imperative
Stability margin must be verified before any supersonic flight
Team 207's approach: replace empirical rules of thumb with a full physics-based aeroelastic solver validated against composite laminate theory

## Slide 4
Physical System: Flight Hardware Fins
T700/epoxy trapezoidal composite fins — actual flight geometry
4 / 13
Team 207 • ITBA • IREC 2026
Fin Geometry
Root chord (cᵣ)
300 mm
Tip chord (cₜ)
150 mm
Semi-span (b)
160 mm
LE sweep angle (Λ)
57.4°
Thickness (t)
6.0 mm
Material & Laminate
Fiber system
T700/Epoxy
Fiber volume fraction
50.19%
Axial modulus E₁
117.2 GPa
Transverse E₂
7.23 GPa
Shear modulus G₁₂
3.47 GPa
Ply count
18 (symmetric)
Density ρ
1580 kg/m³
Tailored layup: alternating DB300 NCF biaxial (±65°/∓25° from chord) and GA90R woven plies (20° from chord) — engineered for D₁₆ bending-torsion coupling

## Slide 5
Theoretical Framework: Three Coupled Pillars
Each pillar feeds into the unified flutter eigenvalue solver
5 / 13
Team 207 • ITBA • IREC 2026
Pillar I
Classical Lamination
Theory (CLT)
Transforms ply-level fiber-matrix constants through 18 plies to yield the complete ABD bending stiffness matrix — including the critical D₁₆ bending-torsion coupling term
Ref: Jones 1999, Reddy 2004
Pillar II
Q4 Mindlin-Reissner
Shell FEM
Bilinear quadrilateral shell elements with selective reduced integration (2×2 membrane/bending, 1×1 shear) over a 24×12 mesh — extracts natural frequencies and mode shapes
Ref: Bathe 1996, Hughes 2000
Pillar III
Supersonic Piston
Theory
Lighthill (1953) / Ashley-Zartarian (1956): local pressure proportional to local normal surface velocity, corrected for Prandtl-Glauert compressibility; GAF matrix by quadrature
Ref: Lighthill 1953, Ashley & Zartarian 1956

## Slide 6
Classical Lamination Theory: Bending Stiffness Matrix
18-ply symmetric T700/epoxy laminate — aeroelastic tailoring via D₁₆ coupling
6 / 13
Team 207 • ITBA • IREC 2026
CLT Analysis Pipeline
1
Compute reduced stiffness Q̄ᵢⱼ for each ply using fiber-matrix rule of mixtures (E₁=117.2 GPa, E₂=7.23 GPa, G₁₂=3.47 GPa, ν₁₂=0.275)
2
Transform Q̄ᵢⱼ through ply orientation angles (±65°/∓25° biaxial, 20° woven) into the laminate coordinate frame
3
Integrate through thickness zₖ boundaries of all 18 plies to form the 6×6 ABD stiffness matrix
4
Extract D sub-matrix: governs bending response — D₁₆ term encodes bending-torsion coupling for aeroelastic tailoring
Computed Bending Stiffness D [N·m]
D₁₁
822.0
D₁₂
264.3
D₁₆
16.35
D₁₂
264.3
D₂₂
869.0
D₂₆
11.65
D₁₆
16.35
D₂₆
11.65
D₆₆
289.8
D₁₆ = 16.35 N·m — bending-torsion coupling coefficient engineered into the layup. This is the primary aeroelastic tailoring parameter.

## Slide 7
Q4 Mindlin-Reissner Shell Finite Element Model
24×12 mesh with selective reduced integration — extracts structural dynamics of clamped fin
7 / 13
Team 207 • ITBA • IREC 2026
FEM Configuration
Element type
Q4 Mindlin-Reissner shell
Mesh
24 × 12 elements
DOF per node
6 (u, v, w, θₓ, θᵧ, θᵤ)
Total DOF
~1,950
Root BC
All root nodes fully clamped
Shear integration
1×1 Gauss (anti-locking)
Membrane/bend
2×2 Gauss quadrature
Mass matrix
Lumped from areal density
Drill stiffness
k = 1×10⁻³ · Eₑff · t · A
Modal Analysis Results (6 Structural Modes)
M1
First bending
174.62 Hz
M2
Second bending
437.72 Hz
M3
First torsion
986.29 Hz
M4
Coupled bend-torsion
1,075.10 Hz
M5
Third bending
1,664.02 Hz
M6
Higher coupled mode
2,051.10 Hz
Mode 1 (174.62 Hz) is critical — lowest frequency mode most susceptible to aerodynamic coupling

## Slide 8
Supersonic Aerodynamics & Flutter Solver
Piston theory + quasi-steady eigenvalue flutter criterion
8 / 13
Team 207 • ITBA • IREC 2026
Supersonic Piston Theory
Aerodynamic pressure at each surface point:
p = (2q∞ / β) · (∂w/∂x + ikw̄/b_ref)
β = √(M² - 1) — Prandtl-Glauert factor
k = ωb/V — reduced frequency
q∞ = ½ρV² — flight dynamic pressure
GAF matrix Q(k) computed by quadrature over FE mesh at k = [0, 0.01, 0.05, 0.1, 0.2, 0.5, 1.0]
Hermitian symmetrisation removes numerical skew.
Quasi-Steady Flutter Solver
1
Form aeroelastic stiffness K_ae(q) = K_struct − q · Q_avg
2
Compute eigenvalues of K_ae at each of 246 supersonic flight points
3
Flutter onset: smallest eigenvalue changes sign (negative → unstable)
4
Stability Margin SM = q_critical / q_flight ; SM = ∞ if all eigenvalues remain positive
ISA Atmosphere Model: ρ(h), a(h), T(h), P(h) computed at each altitude for correct dynamic pressure and Mach-dependent β — troposphere + lower/upper stratosphere regimes

## Slide 9
Flutter Analysis Results: Full Supersonic Envelope
246 flight points evaluated — all conditions flutter-free
9 / 13
Team 207 • ITBA • IREC 2026
246
Supersonic flight points
evaluated
Mach 1.00 – 1.85
∞
Flutter Stability Margin
at every point
SM = q_crit / q_flight
0
Sign changes detected
in eigenvalue spectra
No flutter onset found
174.6 Hz
Fundamental natural
frequency (Mode 1)
First bending mode
Modal Frequencies — Structural Stiffness Summary
Mode 1
174.62 Hz
Mode 2
437.72 Hz
Mode 3
986.29 Hz
Mode 4
1,075.10 Hz
Mode 5
1,664.02 Hz
Mode 6
2,051.10 Hz
Result: The fin is unconditionally stable — aerodynamic forces are purely stiffening throughout the entire supersonic flight envelope

## Slide 10
Physical Interpretation: Dual Wash-Out Mechanism
Why SM = ∞ — the physics behind unconditional stability
10 / 13
Team 207 • ITBA • IREC 2026
Mechanism 1: Geometric Wash-Out
Leading-edge sweep Λ = 57.4°
When the fin deflects outward under aerodynamic bending load, the highly swept planform geometry induces a nose-down twist about the elastic axis.
This reduces the local effective angle of attack → reduces the aerodynamic load → reduces the bending deflection.
Negative feedback loop:
Deflection → reduced load → reduced deflection
Mechanism 2: Material Wash-Out (D₁₆)
Bending-torsion coupling D₁₆ = 16.35 N·m
When the composite laminate bends outward, the engineered D₁₆ coupling in the ABD matrix simultaneously drives a torsional response.
This torsion is oriented to twist the leading edge nose-down, amplifying the stabilizing effect of geometric wash-out.
Combined result:
Aerodynamic forces are purely stiffening — they cannot excite flutter
Together: K_ae = K_struct − q·Q_avg remains positive-definite for all q → no flutter eigenvalue crossing possible

## Slide 11
Computational Pipeline: Eight-Step MATLAB Solver
Automated aeroelastic analysis from laminate config to stability envelope
11 / 13
Team 207 • ITBA • IREC 2026
Step 1
Load Inputs
lam.json (18-ply laminate), flight_data.csv (trajectory)
Step 2
ISA Atmosphere
Compute ρ, a, T, P at each altitude — troposphere + stratosphere
Step 3
Filter Supersonic
Select M ≥ 1.0 flight points (246 of full trajectory)
Step 4
Assemble FEM
Build K, M matrices over 24×12 Q4 mesh with CLT stiffness
Step 5
Modal Analysis
Extract 6 natural frequencies & mode shapes via eigenvalue decomposition
Step 6
Compute GAF
Piston theory: Q(k) at k=[0,0.01,0.05,0.1,0.2,0.5,1.0] by quadrature
Step 7
Flutter Solver
Eigenvalues of K_ae(q) at all 246 points — detect sign changes
Step 8
Results & Plots
Flutter envelope, divergence spectrum, mode shapes, stability margin

## Slide 12
Conclusions
01
A complete three-pillar aeroelastic solver (CLT + Shell FEM + Piston Theory) has been built in MATLAB and applied to flight-hardware composite fins.
02
All 246 supersonic flight points from Mach 1.00 to 1.85 are unconditionally flutter-free — stability margin SM = ∞ at every condition.
03
The stability is physically explained by a dual wash-out mechanism: 57.4° geometric wash-out from sweep + material wash-out from D₁₆ = 16.35 N·m bending-torsion coupling.
04
The approach demonstrates that composite aeroelastic tailoring is a practical, computationally accessible tool for intercollegiate rocketry.
Expected at IREC 2026: flight trajectory reconstruction and post-flight structural assessment to complete computational validation

## Slide 13
Thank You
Questions & Discussion
CLT + FEM + Piston Theory
Theoretical pillars
246 Points • SM = ∞
Flutter analysis result
Dual Wash-Out
Physical stabilizing mechanism
Team 207 • Instituto Tecnológico de Buenos Aires • IREC 2026